City of Brewster

Emergency Water Supply Plan

Adopted in by Ordinance 242,

June 1989, Updated December 2017

Pursuant to the requirements of K.A.R. 28-15-18, the City of Brewster,

has compiled the following information and guidelines for the purpose of implementing an Emergency Water Supply Plan.

Section I				Purpose

Section II				Description

Section III				Disaster Organization

Section IV				Mutual Aid Agreement

Section V				Inventory of Emergency Equipment Available

Section VI				Vulnerability of System (Disaster Response)

Section VII				Water Rationing

Section VIII				Emergency Contacts

Section IX				Annual Review

Section I.	Purpose

The purpose of this plan is to isolate and conserve an adequate supply of potable water during emergency conditions that will be used only to sustain human life and the lives of pets and maintain standards of hygiene and sanitation.

The City of Brewster having adopted along with the Emergency Water Supply Plan include the following  programs:

•	Well Head Protection Plan (adopted by committee1996 with Ground Water Management District #4 and Local Environmental Protection Group out of Colby) to include the 80 acres of land adjoining the west side and 80 acres south of the City limits of the City of Brewster as the Well Head Protection Area. Area selected was due to model presented by GWM#4 on zone of influence to our water supply.

•	Source Water Protection Plan (approved by KDHE in 2003)

•	Water Conservation Plan(Ord. 242 passed 6-13-1989)

•	Water Drought/Emergency Plan (Ord. 304 passed 1-11-2011)

Section II.	Description

The potable water supply for the City of Brewster is obtained through water wells listed as wells 1,2 and 4.

How is water produced:

Water wells from Brewster are in corporate city limits and use vertical turbine pumps equipped with electric motors with reserve power sources on two wells.  Those wells include a 300ci Ford on Well #2 and PTO gearhead for a tractor on Well #4.  Water is then pumped to the storage tank.

Where are water wells located:

Our water supply is the Ogallala aquifer and location:

Well #1 located at 201 First St.

Well #2 located at 203 First St.

Well #4 located at 204 Oklahoma Ave.

How much water is produced from each well:

Water well #1 produces 87 gmp with 50# head

Water well #2 produces 75 gpm with 50# head

Water well #4 produces 325 gpm with 50# head

Storage system and supply:

Brewster’s water system is an above ground storage system capable of holding 50,000 gallons of potable water located at the corner of First St. and Nebraska Ave. Brewster also has a pressure relief valve capable of emergency use for supplying water to the mains and relieving pressure after use is met.  This pressure device can be adjusted for lower or higher pressures.

Booster information:

City of Brewster has no boosters in the system at this time.

Line Size:

The City of Brewster has 4” cast iron mains on primary lines.  The other lines include 4” ductile iron, 4” C-900, 2” cast iron,  2” pvc schedule 40.

Other connection:

The City of Brewster has no other outside source water or services from other public water services or Rural Water Districts.

# Section III.	Disaster Organization

- Mayor – In-Charge Overall or designee in the event of absence.  City Superintendent or appointed person shall oversee all municipal services.

Responsibilities shall include and not be limited to:

- Preserve the safety and welfare of the public with priorities of: Water, Wastewater, Food and Shelter.

1.	Coordinate and direct efforts of maintenance personnel in repair of damage.

2.	Establish communications within the governing body, local news media, and general public.

3.	Establish command posts, medical posts, shelters, etc. while working with the County Emergency Preparedness Personnel.

4.	Assess damages and establish communication with the Mayor and other officials.

5.	Notify KDHE District Engineer (785-625-5663) or Bureau of Water and request assistance as needed.

6.	Oversee any repairs or alterations from the source of supply to treatment and pumping to throughout the distribution system.

7.	Request emergency equipment / supplies if needed.

8.	Request work assistance if needed.

9.	Contact Midwest Energy Company as to loss of power (EMERGENCY NUMBER OF 800-222-3121).

# Section IV.	Mutual Aid Agreement

- Cooperative arrangement for water supply including City of Colby, City of Goodland, Sherman County or others as offered and working with the Thomas County Emergency Preparedness Personnel to help coordinate an effective and efficient process. Their offices will assist the City of Brewster in supplying potable water until our system is safely secured and on line again whereby the City shall be able to provide safe water for the citizens of Brewster.

- Cooperative arrangements for water and wastewater repair parts and fittings, if needed,  have been made with neighboring water districts and cities.

C.  	Mutual Aid Agreements are being drafted currently.

# Section V.	Inventory of Emergency Equipment Available

- City owned equipment:

1.  Brewster Fire Station has a independent generator plant (7000 	watts) supplied with natural gas and the City of Brewster has a      	5,000 watt portable unit.

2.	5205 JD tractor with pallet forks and loader.

3.	Retrieval winch assembly with fall protection and harness

4.  Fire fighting equipment and personnel protective gear

5.  10,000 lbs electric winch (currently not mounted).

6.  4” trash pump, 3” trash pump.

7. 1986 Ford 9000 pumper fire truck

8. 1955 Ford pumper fire truck (standby only)

### Optional Locally owned equipment and supplies:

1.  Payloaders    (Ag Sun LLC,  Carpenter Cattle Co.)

2.  112 Cat Road Grader and Mx 135 tractor w loader, (West Hale              	Township)

3.  Water supply tanks and delivery trucks (Frontier Ag and ADM 	elevators)

4.  Portable PTO driven and gas powered generators (farmers)

5.  Irrigation water wells (Farmers)

6.  Sherman County Rural fire dept. has 3 trucks available in Brewster 	at the local fire station.

### Equipment available through the State of Kansas

1.	Chlorinators (through KDHE and KRWA)

2.	Federally owned units such as portable filter plants, portable storage tanks, etc. (through Bureau of Water Supply) and National Guard.

Section VI.	Vulnerability of System (Disaster Response)

### Drought- Water Shortage-As determined by the Mayor and or City Council

1.	The City’s Ordinance will go into effect regulating the non-essential use of water during an emergency upon authorization from the Mayor and or Council.

2.	Public and media notification of water conservation will be relayed.

3.	Attempt to obtain water from, County Emergency Preparedness.

### Accidental Spills or Contamination

5.  Mayor or Public official shall contact 911.

6.	Mayor or Public official will assess the situation and notify KDHE, Regional EPA Office, or Office of Emergency Preparedness of extent of damage.

7.	Establish communications through the Thomas County Sheriff’s Office, fire, news media, and general public.

8.	The City Superintendent or designated official shall make sure that all sources of uncontaminated water and work to ensure that the potable water storages are full.

9.	When or if hazardous substances contaminate the water supply at the well location, the Superintendent or designee shall stop raw water from being pumped from that location until review and secured.

10.	Utilize if possible the 50,000 gallon storage tank supply.

11.	Upon direction of Mayor, the City shall purchase bottled water for consumption or provide water from alternate source to the public.

12.	Transport water into City from another source if needed.

### Treatment Plant and Auxiliary Power

13.	Power outage due to natural or man-made disaster.

a.	The City will utilize a generator and restore electricity to water and wastewater systems as needed.

b.	The City will ascertain from the Midwest Energy officials when power will be restored.

14.	Excessive damage to City and Buildings

a.	City Mayor, council or appointed agent will assess damages and establish communication with news media and general public.

b.	The City’s ordinance will go into effect regulating the non-essential use of water during an emergency upon recommendation by the licensed water operator and authorization from the Mayor or designee .

c.	Upon direction of Mayor, the City Superintendent will notify KDHE and Bureau of Water of any anticipated needs.

d.	The City Superintendent or officials will isolate distribution system and utilize water storage.

e.	The Mayor, will authorize a work force to repair damages to bring plant or plants back on line.

### Distribution System

15.	Transmission Main Damage

a.	Isolate main and repair.

16.	Storage Tank Damage

a.	The City’s Ordinance will go into effect regulating the non-essential use of water during an emergency upon authorization from the Mayor, council or Superintendent, if needed.

b.	Isolate tank by closing valve at bottom of tank.

c.	Place needed pressure gauges and relief valves on hydrants for wasting in order to maintain a constant pressure.

d.	Contact tower Maintenance Company.  Utility Service Contractors from Pittsburg, Ks.

### Terrorist Threats

17.	Notify Operator and Sheriffs office of threat and coordinate with civil defense personnel to provide protection at POE, booster station, and storage tank.

### Radioactive Fallout

18.	Contact Office of Emergency Preparedness for information as to the possibilities of contamination to the system.

19.	 The City’s ordinance will go into effect regulating the non-essential use of water during an emergency upon authorization from the Mayor, council or Superintendent, if needed.

.

20.	Utilize stored water until system is okay for use

# Section VII.	Water Rationing

- Refer to City Ordinance in Article 4 Section15-401 in the Water Conservation section.

Section VIII. 	Emergency Contacts

### City Contacts

- MAYOR, Rex Jamison	                      		785-694-8114 mobile

- City Superintendent, Mike Schultz			785-462-1447 mobile

- City Clerk, Daryl Ann Jorgensen 				785-694-2268 home

- City Superintendent Office					785-694-2205

Fax     			785-694-2811

### Emergency Services

- Thomas County Sheriff 				785-460-4570 or 911

- Thomas County EMT		Dial         			911

- Thomas County Emergency 				785-460-4516

(Management office)

- Thomas County Health Dept.    				 785-460-4596

- Thomas County Highway Dept.				 785-460-4562

### Federal and State Agencies

Kansas Department Health & Environment			785-625-5663

NW District Office- Hays

Kansas Department Health & Environment			785-296-5503

Public Water Supply Section- Topeka

Kansas Adjutant General Department		          		 785-274-1409

Division of Emergency Management- Topeka

Environmental Protection Agency				913-551-7423

Region 7- Kansas City, KS

Kansas Rural Water Association				785-336-3760

Homeland Security						1-800-237-3239

### Services:

- Communications - S&T Telephone Cooperative	 785-694-2256

- Electrical and Gas – Midwest Energy, Colby, Ks 	785-462-8251

- Fuel – Frontier Ag 785-694-2281, Brewster LLC    	785-694-4007

- Repair Mechanic – TJ’s Tire, Tom Aschennbrenner	 785-694-2213

- Food –   Local restaurant 785-694-2727,

Local grocery store at 785-694-2824

- Housing – Unavailable multiple units, Hotels Colby or Goodland.

- Health – Brewster EMS *911* and Colby Medical and Surgical Center, Colby, Ks.

- Lumber – Colby Lumber and  in Colby, Ks.

- Water/Sewer repairs- Hajoca, Colby Ks 785-462-6731

### Media

- Rocking M. Radio-KXXX / KQLS radio Colby, Ks. 785-462-3305

- Colby Free Press (Official newspaper)	785-462-3963

# Section IX.	Annual Review

Annual Review Sign Off Sheet:

It shall be required that this policy be reviewed annually by the City of Brewster Mayor and City Council and City Superintendent.

| Date Reviewed | Signature of Mayor | Signature of Operator |
| --- | --- | --- |
| 1-09-2018 |  |  |